## Slide 1: ESnet Science DMZ & Pilot Efforts
Energy Sciences Network (ESnet)
Lawrence Berkeley National Laboratory
Jason Zurawski – zurawski@es.net
Hackathon
February 28th, 2017

## Slide 2: Outline
ESnet Overview
Why is Networking Hard?
Efficiently Moving Bits (e.g. the ‘Science DMZ’)
Pilot @ APS’s GM/CA
Open Call

## Slide 3: ESnet Background
ESnet is a special-purpose mission network, funded by the US Congress to support scientific goals of the Department of Energy.
We see networking as a means to an end: scientific productivity.
We aim to create a world in which discovery is unconstrained by geography.

## Slide 4
56 PB in Jan 2017
This is just R&E related traffic (e.g. not combined with commodity peering)

## Slide 5
Network as Infrastructure Instrument
Connectivity is the first step – usability must follow

## Slide 6
80% of ESnet traffic originates or terminates outside the DOE complex.
ESnet’s success is necessary but not sufficient for DOE, because networks share fate. SC invests nearly $1B/year in university research: campus networks matter.

## Slide 7: Outline
ESnet Overview
Why is Networking Hard?
Efficiently Moving Bits (e.g. the ‘Science DMZ’)
Pilot @ APS’s GM/CA
Open Call

## Slide 8: Motivation
Networks are an essential part of data-intensive science
  Connect data sources to data analysis
  Connect collaborators to each other
  Enable machine-consumable interfaces to data and analysis resources (e.g. portals), automation, scale
Performance is critical
  Exponential data growth
  Constant human factors
  Data movement and data analysis must keep up
Effective use of wide area (long-haul) networks by scientists has historically been difficult
Notes: Human factors – attention span, ability to manage complexity – these are constant
There is a huge amount of promise in data-intensive science. Effective use of networks can help realize those benefits.
The Science DMZ model helps address the difficulties scientists often experience with using networks.

## Slide 9: TCP – Ubiquitous and Fragile
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Packet loss in conjunction with latency is a performance killer
  Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)
Notes: The application sees the network as a socket.
The socket interface does not provide path diagnostics or other troubleshooting information.
TCP behaves as it does because of measures taken in the 1980s to fix the congestion collapse of the Internet
TCP makes a promise to the application – TCP will get the data to the other end, or TCP will return an error. TCP makes no promises about performance.

## Slide 10: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
Notes: This is an annotated version of the plot from the Science DMZ paper
Beyond your metro area, zero loss is essentially required for high performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 11: Working With TCP In Practice
Far easier to support TCP than to fix TCP
  People have been trying to fix TCP for years – limited success
  Like it or not we’re stuck with TCP in the general case
Pragmatically speaking, we must accommodate TCP
  Sufficient bandwidth to avoid congestion
  Zero packet loss
  Verifiable infrastructure
    Networks are complex
    Must be able to locate problems quickly
    Small footprint is a huge win – small number of devices so that problem isolation is tractable
Notes: Do not underestimate the value of three TCP improvements:
RFC1323 (window scaling)
Kernel autotuning
Improved congestion algorithms
However, loss + latency is still a performance killer.
TCP must be accommodated – this is our job as engineers and architects

## Slide 12: Outline
ESnet Overview
Why is Networking Hard?
Efficiently Moving Bits (e.g. the ‘Science DMZ’)
Pilot @ APS’s GM/CA
Open Call

## Slide 13: The Science DMZ in 1 Slide
Consists of three key components, all required:
“Friction free” network path
  Highly capable network devices (wire-speed, deep queues)
  Virtual circuit connectivity option
  Security policy and enforcement specific to science workflows
  Located at or near site perimeter if possible
Dedicated, high-performance Data Transfer Nodes (DTNs)
  Hardware, operating system, libraries all optimized for transfer
  Includes optimized data transfer tools such as Globus Online and GridFTP
Performance measurement/test node
  perfSONAR
Engagement with end users
  Details at http://fasterdata.es.net/science-dmz/
© 2013 Wikipedia
Notes: Single slide summary

## Slide 14: Local And Wide Area Data Flows
Notes: The green data path is susceptible to TCP performance problems stemming from packet loss combined with long distances
The red data path is very low latency – loss matters much less here (though too much loss will still cause problems)
Remember the throughput vs. latency graph

## Slide 15: Dedicated Systems – Data Transfer Node
The DTN is dedicated to data transfer
Set up specifically for high-performance data movement
  System internals (BIOS, firmware, interrupts, etc.)
  Network stack
  Storage (global filesystem, Fibrechannel, local RAID, etc.)
  High performance tools
  No extraneous software
Limitation of scope and function is powerful
  No conflicts with configuration for other tasks
  Small application set makes cybersecurity easier
Notes: All aspects of the DTN must be tuned – even the BIOS matters
Limit the scope of the DTN as well – its job is data movement, its job is not to have office software on it.
Craft a specific security profile/policy around its only task.

## Slide 16: Data Transfer Tool Comparison
In addition to the network, using the right data transfer tool is critical
Data transfer test from Berkeley, CA to Argonne, IL (near Chicago). RTT = 53 ms, network capacity = 10Gbps.
    Tool Throughput
    scp: 140 Mbps
    HPN patched scp: 1.2 Gbps
    ftp 1.4 Gbps
    GridFTP, 4 streams 5.4 Gbps
    GridFTP, 8 streams 6.6 Gbps
    Note that to get more than 1 Gbps (125 MB/s) disk to disk requires properly engineered storage (RAID, parallel filesystem, etc.)
Notes: Comparison of legacy and recommended tools.
Note that rsync over HPN-SSH is reasonable in a 1Gbps environment – if you are stuck with rsync over SSH, at least use HPN-SSH.
Globus is now deployed at a large number of major scientific sites – the basic data transfer functionality is free.

## Slide 17: Outline
ESnet Overview
Why is Networking Hard?
Efficiently Moving Bits (e.g. the ‘Science DMZ’)
Pilot @ APS’s GM/CA
Open Call

## Slide 18: GM/CA
General Medical Sciences and Cancer Institutes Structural Biology Facility @ APS
  Focused on the study of crystallographic structure determination of biological macromolecules by X-ray diffraction
Typical User:
  Visits and spends some allocated time with samples and the beamline machinery
  Mails samples, controls device remotely
  In either case – data has to go ‘somewhere’

## Slide 19
By 2025, DOE light sources will be transformed by high-resolution detectors, advanced mathematical analysis techniques, robotics, software automation, programmable networks.
Detectors capable of generating terabit data streams.
Computational tools for analysis, data reduction, feature extraction in situ, using advanced algorithms and specialized hardware.
Increased scientific throughput from robotics and automation software.
Data management and sharing, with federated identity management and flexible access control.
Post-processing: reconstruction, inter-comparison, simulation, visualization.
Integration of experimental and computational facilities in real time, using programmable networks.
Superfacility instances multiply.

## Slide 20: Current Design

## Slide 21: Current Design

## Slide 22: ANL Border to ESnet New York (perfSONAR Test)

## Slide 23: GM/CA to ESnet New York (perfSONAR Test)

## Slide 24: GM/CA to ANL Border (perfSONAR Test)

## Slide 25: Pilot Network
Plan:
  Use campus and building fiber resources for 2nd path
  Applies to only a limited set of resources (perfSONAR, DTN)
Benefits
  Bypass congested local infrastructure
  Apply targeted (vs. blanket) security policy
Cautions:
  Prevent just ‘anything’ from using fast path – policy to control this
  Still need to figure out cause of local issues (e.g. this isn’t a pave over)

## Slide 26: perfSONAR Results

## Slide 27: perfSONAR Results

## Slide 28: perfSONAR Results

## Slide 29: perfSONAR is One Metric – what about GridFTP?
Setup of the DTN Architecture:
  2 Servers
  Shared filesystem
  Each server has 2 interfaces/routes:
    Science DMZ routes (plumbed to specific external locations via ANL, ESnet/MREN) and avoiding slower path
    Traditional routes over slower path
  Goal: show that with the correct network the *SAME* underlying infrastructure can perform as well as the perfSONAR testing

## Slide 30: Testing ESnet CERN (long RTT) to GMCA
Scale is Mbps
Across the board improvement of around 5x-20x
Exercise helped to tune filesystem performance.
Chart: 
| 10G (single file) | 50G (single file) | 100G (single file) | 500G (single file) | 50G (medium files & deep dirs) | 150G (medium files & shallow dirs) | 500G (large files)
GMCA idb DMZ | 987.654 | 1238.39 | 1362.862 | 1164.822 | 587.717 | 1265.823 | 944.241
GMCA idb | 289.855 | 263.505 | 264.201 | 290.255 | 118.871 | 180.234 | 45.793

## Slide 31: Testing GMCA to ESnet CERN (long RTT)
Metadata operations (e.g. deeply nested directories) coupled with smaller files remains hard to crank up
Chart: 
| 10G (single file) | 50G (single file) | 100G (single file) | 500G (single file) | 50G (medium files & deep dirs) | 150G (medium files & shallow dirs) | 500G (large files)
GMCA idb DMZ | 1142.857 | 1290.323 | 1353.638 | 1251.956 | 574.713 | 1229.508 | 2960.77
GMCA idb | 300.752 | 322.061 | 266.667 | 246.945 | 190.749 | 211.268 | 420.315

## Slide 32: Testing GMCA to ESnet LBL (medium RTT)
Metadata operations (e.g. deeply nested directories) coupled with smaller files remains hard to crank up
Chart: 
| 10G (single file) | 50G (single file) | 100G (single file) | 500G (single file) | 50G (medium files & deep dirs) | 150G (medium files & shallow dirs) | 500G (large files)
GMCA idb DMZ | 1000 | 1219.512 | 1228.879 | 1688.476 | 756.144 | 2127.66 | 3642.987
GMCA idb | 509.554 | 307.929 | 104.167 | 251.889 | 122.474 | 650.407 | 1117.006

## Slide 33: Future
Wider use @ APS
  Solution now goes directly to a specific beamline – how to support the entire facility?
Wider use @ ANL
  Service for other research groups (e.g. ALCF, ARM, etc.)
  Pool of DTN resources w/ Globus, instead of each group manning their own (allows to back up to communal storage)
Defining Policy
  ACLs – ports exposed for things like perfSONAR, Globus. Shut off for things that don’t need it. Gray area is defining what is and is not science.
  Who gets on, who doesn’t
  Managing routing @ the border to best utilize the available WAN links

## Slide 34: APS Science DMZ Pilot
What about to user networks? Trial tests to (excited) Universities:
  Stanford: Installed a dedicated ‘Science DMZ’ connection in the APS user’s lab at Stanford (bypasses institutional firewalls)
  Purdue: Worked well … since they already had a Science DMZ 
  Rice: Seeking NSF and institutional funding (and using the APS user as a pilot) to install a campus-wide Science DMZ
Trial test to (less excited) Universities:
  Michigan: Acknowledged internal network issues, expected resolution is mid 2017.
  Minnesota: Was not able to provide updated test data.
  USC: Was not able to provide updated test data.
Takeaways: Building a DMZ at a Lab/Facility is only the first step. We all share fate when it comes to scientific data movement, and improving outcomes at universities ‘raises all boats’.

## Slide 35: Outline
ESnet Overview
Why is Networking Hard?
Efficiently Moving Bits (e.g. the ‘Science DMZ’)
Pilot @ APS’s GM/CA
Open Call

## Slide 36: Science Engagement Vision – Revisited
Building on the success of Science DMZ, work with collaborators and partners at DOE, DOE labs, academia and industry to imagine a new standardized “service” or architecture model that would greatly simplify the methods for scientists to access, analyze, move and store data without IT intervention or ad hoc engineering heroics.
This means working together to move many “prototype” workflow and portal technologies into production.

## Slide 37: Extending the Idea of the APS Pilot
Other Beamlines?
Other Labs?
engage@es.net

## Slide 38: LANL Example - Putting Theory into Practice
Discussion:
  Security of the enclave
  perfSONAR Testing Strategies
  Locating a scientific user
  Identifying traffic patterns over ESnet to other DOE sites
  Use of OSCARS
  Appropriate hardware for the network layer

## Slide 39: LANL Testimonial
Heightened ESnet awareness generating questions like:
  Who is our ESnet representative?
  What it the ESnet SLA?
Stimulated inter-organization communication on network design
  This is his indicator of workshop success
  Met to review plans for diverse fiber path and backup ESnet connection
  Identified special needs for gene sequencers
“perfSONAR keeps coming up in hallway conversations. The discussions range from testing new designs to before-and-after measurement to diagnosing problems in today's production network.”
“The workshop was well received from everyone I talked to. We have a better, shared understanding on how to support science”

## Slide 40: ESnet Science DMZ & Pilot Efforts
Energy Sciences Network (ESnet)
Lawrence Berkeley National Laboratory
Jason Zurawski – zurawski@es.net
Hackathon
February 28th, 2017